For switch and vlan conf

configure terminal
no ip domain-lookup
vlan 10
exit
vlan 20
exit
vlan 30
interface fastEthernet 0/2
switchport mode access
switchport access vlan 10
exit
interface fastEthernet 0/3
switchport mode access
switchport access vlan 20
exit
interface fastEthernet 0/4
switchport mode access
switchport access vlan 30
exit
interface fastEthernet 0/1
switchport mode trunk
switchport trunk native vlan 1
switchport trunk allowed vlan 10
switchport trunk allowed vlan add 20
switchport trunk allowed vlan add 30
exit

ospf of batiment 1
ROUTER 0
router ospf 1
network 192.168.1.0 0.0.0.7 area 0
network 192.168.1.8 0.0.0.7 area 0
network 192.168.1.16 0.0.0.7 area 0
network 192.168.1.100 0.0.0.3 area 0
ROUTER 1
router ospf 1
network 192.168.1.24 0.0.0.7 area 0
network 192.168.1.32 0.0.0.7 area 0
network 192.168.1.40 0.0.0.7 area 0
network 192.168.1.100 0.0.0.3 area 0
network 192.168.1.200 0.0.0.3 area 0

ROUTER 2
router ospf 1
network 192.168.1.48 0.0.0.7 area 0
network 192.168.1.56 0.0.0.7 area 0
network 192.168.1.64 0.0.0.7 area 0
network 192.168.1.160 0.0.0.3 area 0
network 192.168.1.200 0.0.0.3 area 0

ROUTER 3
router ospf 1
network 192.168.1.72 0.0.0.7 area 0
network 192.168.1.80 0.0.0.7 area 0
network 192.168.1.88 0.0.0.7 area 0
network 192.168.1.160 0.0.0.3 area 0
network 192.168.6.0 0.0.0.255 area 0
network 192.168.7.0 0.0.0.255 area 0

batiment B:

first router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.2.1 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.2.9 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.2.17 255.255.255.248
no shutdown
exit

second router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.2.25 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.2.33 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.2.41 255.255.255.248
no shutdown
exit

third router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.2.49 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.2.57 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.2.65 255.255.255.248
no shutdown
exit

fourth router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.2.73 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.2.81 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.2.89 255.255.255.248
no shutdown
exit

ospf of batiment B

router ospf 1
network 192.168.2.0 0.0.0.7 area 0
network 192.168.2.8 0.0.0.7 area 0
network 192.168.2.16 0.0.0.7 area 0
network 192.168.2.100 0.0.0.3 area 0
end
router ospf 1
network 192.168.6.0 0.0.0.255 area 0
network 192.168.8.0 0.0.0.255 area 0

router ospf 1
network 192.168.2.24 0.0.0.7 area 0
network 192.168.2.32 0.0.0.7 area 0
network 192.168.2.40 0.0.0.7 area 0
network 192.168.2.100 0.0.0.3 area 0
network 192.168.2.200 0.0.0.3 area 0

router ospf 1
network 192.168.2.48 0.0.0.7 area 0
network 192.168.2.56 0.0.0.7 area 0
network 192.168.2.64 0.0.0.7 area 0
network 192.168.2.160 0.0.0.3 area 0
network 192.168.2.200 0.0.0.3 area 0

router ospf 1
network 192.168.2.72 0.0.0.7 area 0
network 192.168.2.80 0.0.0.7 area 0
network 192.168.2.88 0.0.0.7 area 0
network 192.168.2.160 0.0.0.3 area 0

batiment C:

first router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.3.1 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.3.9 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.3.17 255.255.255.248
no shutdown
exit

second router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.3.25 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.3.33 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.3.41 255.255.255.248
no shutdown
exit

third router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.3.49 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.3.57 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.3.65 255.255.255.248
no shutdown
exit

fourth router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.3.73 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.3.81 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.3.89 255.255.255.248
no shutdown
exit

ospf of batiment C

router ospf 1
network 192.168.3.0 0.0.0.7 area 0
network 192.168.3.8 0.0.0.7 area 0
network 192.168.3.16 0.0.0.7 area 0
network 192.168.3.100 0.0.0.3 area 0

end

router ospf 1
network 192.168.3.24 0.0.0.7 area 0
network 192.168.3.32 0.0.0.7 area 0
network 192.168.3.40 0.0.0.7 area 0
network 192.168.3.100 0.0.0.3 area 0
network 192.168.3.200 0.0.0.3 area 0

router ospf 1
network 192.168.3.48 0.0.0.7 area 0
network 192.168.3.56 0.0.0.7 area 0
network 192.168.3.64 0.0.0.7 area 0
network 192.168.3.160 0.0.0.3 area 0
network 192.168.3.200 0.0.0.3 area 0

router ospf 1
network 192.168.3.72 0.0.0.7 area 0
network 192.168.3.80 0.0.0.7 area 0
network 192.168.3.88 0.0.0.7 area 0
network 192.168.3.160 0.0.0.3 area 0
network 192.168.9.0 0.0.0.255 area 0
network 192.168.7.0 0.0.0.255 area 0
router ospf 1
network 192.168.10.0 0.0.0.255 area 0

batiment D:

first router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.4.1 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.4.9 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.4.17 255.255.255.248
no shutdown
exit

second router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.4.25 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.4.33 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.4.41 255.255.255.248
no shutdown
exit

third router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.4.49 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.4.57 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.4.65 255.255.255.248
no shutdown
exit

fourth router:

 conf term
interface Fa0/0.10
encapsulation dot1Q 10
ip address 192.168.4.73 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.20
encapsulation dot1Q 20
ip address 192.168.4.81 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.30
encapsulation dot1Q 30
ip address 192.168.4.89 255.255.255.248
no shutdown
exit

ospf of batiment D

router ospf 1
network 192.168.11.0 0.0.0.255 area 0
network 192.168.9.0 0.0.0.255 area 0
network 192.168.8.0 0.0.0.255 area 0

network 192.168.4.0 0.0.0.7 area 0
network 192.168.4.8 0.0.0.7 area 0
network 192.168.4.16 0.0.0.7 area 0
network 192.168.4.100 0.0.0.3 area 0
end

router ospf 1
network 192.168.4.24 0.0.0.7 area 0
network 192.168.4.32 0.0.0.7 area 0
network 192.168.4.40 0.0.0.7 area 0
network 192.168.4.100 0.0.0.3 area 0
network 192.168.4.200 0.0.0.3 area 0
ex

router ospf 1
network 192.168.4.48 0.0.0.7 area 0
network 192.168.4.56 0.0.0.7 area 0
network 192.168.4.64 0.0.0.7 area 0
network 192.168.4.160 0.0.0.3 area 0
network 192.168.4.200 0.0.0.3 area 0

router ospf 1
network 192.168.4.72 0.0.0.7 area 0
network 192.168.4.80 0.0.0.7 area 0
network 192.168.4.88 0.0.0.7 area 0
network 192.168.4.160 0.0.0.3 area 0

administration batiment

For switch and vlan conf

configure terminal
no ip domain-lookup
vlan 40
exit
vlan 50
exit
vlan 60
interface fastEthernet 0/2
switchport mode access
switchport access vlan 40
exit
interface fastEthernet 0/3
switchport mode access
switchport access vlan 50
exit
interface fastEthernet 0/4
switchport mode access
switchport access vlan 60
exit
interface fastEthernet 0/1
switchport mode trunk
switchport trunk native vlan 1
switchport trunk allowed vlan 40
switchport trunk allowed vlan add 50

configuration switch de distribution
configure terminal
no ip domain-lookup
vlan 40
exit
vlan 50
exit
interface fastEthernet 0/1
switchport mode trunk
switchport trunk native vlan 1
switchport trunk allowed vlan 40
switchport trunk allowed vlan add 50
exit

interface fastEthernet 0/2
switchport mode trunk
switchport trunk native vlan 1
switchport trunk allowed vlan 40
exit

interface fastEthernet 0/3
switchport mode trunk
switchport trunk native vlan 1
switchport trunk allowed vlan 40
exit

router

 conf term
interface Fa0/0.40
encapsulation dot1Q 40
ip address 192.168.5.1 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.50
encapsulation dot1Q 50
ip address 192.168.5.9 255.255.255.248
no shutdown
exit

conf term
interface Fa0/0.60
encapsulation dot1Q 60
ip address 192.168.5.17 255.255.255.248
no shutdown
exit

OSPF

router ospf 1
network 192.168.5.0 0.0.0.7 area 0
network 192.168.5.8 0.0.0.7 area 0
network 192.168.12.0 0.0.0.255 area 0
network 192.168.10.0 0.0.0.255 area 0
network 192.168.11.0 0.0.0.255 area 0
network 192.168.5.16 0.0.0.7 area 0

port security for vlans
en
conf term
interface Fa0/2
 switchport mode access
 switchport port-security
 switchport port-security maximum 1
 switchport port-security violation shutdown
 switchport port-security mac-address sticky
  ex
interface Fa0/3
 switchport mode access
 switchport port-security
 switchport port-security maximum 1
 switchport port-security violation shutdown
 switchport port-security mac-address sticky
  ex

vlan ACL

access-list 2 deny host 192.168.1.2
access-list 2 deny host 192.168.1.26
access-list 2 deny host 192.168.1.50
access-list 2 deny host 192.168.1.74
access-list 2 deny host 192.168.2.2
access-list 2 deny host 192.168.2.26
access-list 2 deny host 192.168.2.50
access-list 2 deny host 192.168.2.74
access-list 2 deny host 192.168.3.2
access-list 2 deny host 192.168.3.26
access-list 2 deny host 192.168.3.50
access-list 2 deny host 192.168.3.74
access-list 2 deny host 192.168.4.2
access-list 2 deny host 192.168.4.26
access-list 2 deny host 192.168.4.50
access-list 2 deny host 192.168.4.74
access-list 2 permit any

interface fa0/0.40
ip access-group 2 out
exit
interface fa0/0.50
ip access-group 2 out
exit